| Australian Refrigeration Mechanics Association An association established to support all Refrigeration and Air Conditioning Specialists 38 Ceduna Street, Loganholme QLD 4129 Ph: 0403 680 981 Email: kim@arma.email | RISK ASSESSMENT |
| --- | --- |

| Process/Material/Activity: | Refrigerant Reclaiming – Waste Management Plant – Townsville Council |
| --- | --- |
| Issued By: Kevin Ballment | Date: | Review Due Date: |

| Ref No. | Step 1: Identify the hazard/s | Step 2: Assess the risks - Note there may be several risks associated with each hazard List the Consequence (how bad would it be?), Likelihood & Risk rating for each risk – see Risk Matrix | Step 3 & 4: List the controls needed to remove or reduce the risks and record date completed | Step 5: How will you monitor the risk and check the controls work? Record review date |
| --- | --- | --- | --- | --- |
|  | What could cause harm? | What could go wrong? | C | L | R | Controls | Date completed | Review method | Review Date |
|  | Non-technical competent persons inability to distinguish between Fridge types; Gas Electric – Ammonia & Water | Death, Ammonia causes Asphyxiation, loss of sight or burning of sensory hairs in the nasal passage and throat Environmental Impact Major Costs | 5 | 5 | 10 | Only Trade Qualified / technically competent persons should carry out works on this type of unit |  | NOT TO BE RECLAIMED |  |
|  | Connecting reclaim components to incorrect refrigerant lines. | Exposure to liquid refrigerants resulting in burning of skin or eyes. Environmental Impact Major Costs | 4 | 5 | 9 | This work MUST be carried by a the holder of an RHL (refrigerant handling licence) OR by trained personnel under the supervision of a person who holds an RHL |  |  |  |
|  | Non-technical competent persons inability to distinguish between Refrigerants; LPG used as refrigerants | Death, Serious injury - Exposure to explosion or fire Environmental Impact Major Costs | 4 | 5 | 9 | This work MUST be carried by a the holder of an RHL (refrigerant handling licence) OR by trained personnel under the supervision of a person who holds an RHL |  |  |  |
|  | Failure to maintain correct temperature of Reclaim Bottle | Explosion, fire, death, Environmental Impact Major Costs | 5 | 5 | 10 | This work MUST be carried by a the holder of an RHL (refrigerant handling licence) OR by trained personnel under the supervision of a person who holds an RHL |  |  |  |
|  | Capacitors can and will hold an electrical charge | Electric shock, death | 4 | 4 | 8 | This work MUST be carried by a the holder of an RHL (refrigerant handling licence) OR by trained personnel under the supervision of a person who holds an RHL |  |  |  |
|  | Failure to weigh refrigerant bottles, risk of pressure relief valve venting refrigerant | Refrigerant released into atmosphere, bottle can explode. Death, serious injury and environmental impact | 4 | 4 | 8 | This work MUST be carried by a the holder of an RHL (refrigerant handling licence) OR by trained personnel under the supervision of a person who holds an RHL |  |  |  |

Note: Recovery/Reclamation of refrigerants MUST be carried out in accordance with the Ozone Protection and Synthetic Greenhouse Gas Management Regulations 1995 made under the Ozone Protection and Synthetic  Greenhouse Gas Management Act 1989

and

any relevant Queensland Government Occupational Health and Safety rules and regulations and/or codes of practice including (but not limited to):

Queensland WH&S Act 1995

Queensland Risk Management Code of Practice 2007 (inc supplements 1, 2 and3)

Queensland Hazardous Substances 2003 Code of Practice

Check all Codes of practice and legislation are up to date;

ARMA provide this document as a template only it is your responsibility to ensure all information is correct.

Risk Assessment Matrix

For use with the Risk Management guide

This is one example of a number of tools that can assist with your risk assessment process.

What you need to do

- Consider what can go wrong

- Determine how bad the outcome would be - Consequences

- Determine how likely it is to happen - Likelihood

- Calculate the risk level

| LIKELIHOOD | CONSEQUENCES |
| --- | --- |
|  | Catastrophic 5 | Major 4 | Moderate 3 | Minor 2 | Insignificant 1 |
| Almost certain 5 | 10 | 9 | 8 | 7 | 6 |
| Likely 4 | 9 | 8 | 7 | 6 | 5 |
| Possible 3 | 8 | 7 | 6 | 5 | 4 |
| Unlikely 2 | 7 | 6 | 5 | 4 | 3 |
| Rare 1 | 6 | 5 | 4 | 3 | 2 |

| Risk Score |  | What should I do? |
| --- | --- | --- |
| 9-10 | Extreme | Immediate action required |
| 7-8 | High | Action plan required, senior management attention needed |
| 5-6 | Moderate | Specific monitoring or procedures required, management responsibility must be specified |
| 2-4 | Low | Manage through routine procedures |

CONSEQUENCES: 	How severely could it hurt someone/cause damage?

Catastrophic 		death or large number of serious injuries, environmental disaster,    huge cost

Major			serious injury, extensive injuries, severe environmental damage, major cost

Moderate		medical treatment required, contained environmental impact, high cost

Minor			first aid treatment required, some environmental and/or financial impact

Insignificant		No injuries, low financial/environmental impact

LIKELIHOOD: 	How likely is it to happen?

Almost Certain		expected to occur in most circumstances

Likely 			will probably occur in most circumstances

Possible 		might possibly occur at some time

Unlikely 		could occur at some time

Rare 		          	may occur only in exceptional circumstances

# Endnotes

A Hazard is something with the potential to cause harm, eg manual handling, ergonomic, substance, plant, radiation, vibration, noise, electrical, work environment

Risk is the likelihood that damage/personal injury will occur because of the hazard. Risks are assessed dependent on variables such as how often the situation occurs, how many people are exposed, skills and experience of individuals etc, as well as physical characteristics of the hazard, ie concentrations, speed, position in relation to other hazards etc.

Consequences  can be Catastrophic (Cat), Major (Maj), Moderate (Mod), Minor (Min) Insignificant (Ins)

Likelihood can be Almost certain (AC) likely (L), Possible (P), Unlikely (U), Rare (R)

Risk Rating is obtained from the Risk Matrix

Controls can include eliminating the hazard or minimising the likelihood of risk, eg by substituting a less hazardous substance or process, using training or safe work procedures or provision of Personal Protective Equipment.

Monitor to ensure controls are being used and are sufficiently minimising the risk

Prepared by Kevin Ballment on behalf of ARMA

Kevin Ballment

185 Geaney Lane Deeragun Qld

Ph: 07 4751 5155

Disclaimer

These procedures are for use by ARMA, Queensland.  This information is believed to be reliable and current.  ARMA, makes no guarantee and assumes no responsibility as to the absolute correctness of these procedures in all circumstances or for their suitability for use outside of ARMA.